CFD Lab: Geometry Optimization
M.Sc. Praktikum: Scientific Computing: CFD
Tomaso Bianucci, Olga Glogowska, Keefe Huang
Technische Universität München
Munich, 23.April.2018

---
Background
- Automized geometry optimization has been the end goal of many CFD-based solvers
- Especially relevant due to additive technologies [2]
[2]C. Othmer and T. Grahs, CFD topology and shape optimization with adjoint methods. 2006

---
Background
Fig 1: Geometry Optimization via Drag / Pressure Sensitivities [1]
[1]C. Othmer, “Adjoint methods for car aerodynamics,” Journal of Mathematics in Industry, vol. 4, no. 1, p. 6
,Jun. 2014.

---
Goal & Scope
- Optimize Geometry by:
  - Detecting regions that result in lower flow:
    - Regions with formed vortices
    - Dead zones
    - Regions of high „drag“
  - Updating the CFD solver to update .PGMs and optimize (improve) the geometry and avoid forbidden geometry!

---
Detection: Vortices (Filling)
- Idea from [3]:
  - Identify center of vertex and iteratively identify associated regions
[3]V. Holmén, “Methods for Vortex Identification,” Master’s Theses in Mathematical Sciences, 2012.

---
Detection: Vortices (Filling)
Fig 2: Vortex Center Identification using point velocities [3]

---
Detection: Vortices (Filling)
Fig 3: Vortex growth algorithm [3]

---
Problem: Aggresive Vortex Fill-in
Any region with instability would be flagged as a vortex and filled-in

---
Problem: Aggresive Vortex Fill-In
- Any region with instability would be flagged as a vortex and filled-in
- Solution:
  - Only fill-in vortices of certain size and with certain velocities
  - Only apply vortex detection every k iterations

---
Detection: Dead zones (Filling)
- Initially fixed threshold velocity was used as a threshold to fill-in
- But this was too unstable!

---
Problem: Over-aggresive fill-in
- Problem: What is small?
  - After trial-and-error, using percentage of max velocity was found to be effective
  - Add material at boundaries and prevent material from being repeatedly cheanged
  - Implement additional „budget“ to limit changes to pgm per update iteration

---
Detection: Areas of high „drag“ (Removal)
- Determine pressure and velocity magnitude differences across corners, if differences were too big, fill in region
- Determine if upstream/downstream of flow

---
Implementation: Psuedo-Code
initializeMatrices( … );
for( PGMConvergenceCriteria )
  performSimulation( … );
  fillVortices( …, Flag );
  updatePGM( …, imax, jmax, U, V, P, Flags );
  detectAndFixGeometry( … , imax, jmax, Flags);
  decodeAndWrite_pgm( … , PGM, Flags );
freeMatrices(… );
cleanup( … );
Qunsheng, Huang (TUM) | MsC. Computational Science and Engineering

---
Implementation: Update PGM Psuedo-Code
void updatePGM( … ):
  for(x,y : 1→ imax, jmax)
      if(isObstacle(Flag[x][y])):
        isFlip = checkPressure( … );
        isFlip += checkVelocity( … );
        if(isFlip):
          fliptoFluid(Flag[x][y], … );
      else:
        isFlip = checkDeadZone( … );
        if(isFlip):
          fliptoSolid(Flag[x][y], … );
Qunsheng, Huang (TUM) | MsC. Computational Science and Engineering

---
Case 1: Flow Over Step
- Used a modified flow over step PGM file to see the shifting of the step due to reduce drag
- Used as model case to see vortex fill-in

---
Case 2: Simple Bend
- Used to investigate cases when direction of flow changes during updates
- Performed suprisingly well

---
Case 3: Immersed Obstacle
- Single cube immersed in middle of simulation
- Masking performed at the middle of the obstacle to prevent it from „floating“ away
- Initial Steady-State Outflow: 8.06
- Final Steady-State Outflow: 25.26

---
Case 4:

---
Summary
- Successful implementation of output „maximisation“ - not necessarily optimization
- However, input cases are highly sensative to input factors (ie. Pressure/Velocity threshholds for removal and addition, vortex strength detection etc.)

---
References
- [1]C. Othmer, “Adjoint methods for car aerodynamics,” Journal of Mathematics in Industry, vol. 4, no. 1, p. 6, Jun. 2014.
- [2]C. Othmer and T. Grahs, CFD topology and shape optimization with adjoint methods. 2006.
- [3]V. Holmén, “Methods for Vortex Identification,” Master’s Theses in Mathematical Sciences, 2012.